## Slide 1: Computer architecture and Organization I/O Organization
M. Khademul Islam, PhD Professor, Dept. of CSE, Rajshahi University, Bangladesh Email: khademul.cse@ru.ac.bd, tel: +88-01727-786600 web: www.ru.ac.bd/cse/~mki

## Slide 2: I/O Organization
Peripheral devices
The input or output devices attached to the computer are also called peripherals.
Among the most common peripherals are keyboards, display units and printers
The peripherals that provide auxiliary storage for the system are magnetic disks and tapes.
The devices that are under the direct control of computer are said to be connected online.

## Slide 3: I/O Organization
I/O Interface
Provides the method for transferring information between internal computing unit and external I/O devices.
Interface
I/O interface requires the following things:
  Special hardware components between the CPU and peripherals
  Supervise and synchronize all input and output transfers

## Slide 4: I/O Organization
I/O Bus and Interface Modules
The interface of I/O with CPU is performed by different I/O bus lines  Data lines, Address lines, Control lines:

## Slide 5: I/O Organization
Interface Modules:
SCSI (Small Computer System Interface)
IDE (Integrated Device Electronics)
RS-232
USB (Universal Serial Bus)

## Slide 6: I/O Organization
I/O versus Memory Bus
Computer buses are used to communicate with memory and I/O.
Three ways to make such communication:
Use two separate buses, one for memory and the other for I/O
Use one common bus for both memory and I/O but have separate control lines for each
Use one common bus for memory and I/O with common control lines

## Slide 7: I/O Organization
Synchronous Data Transfer
All data transfers occur simultaneously during
the occurrence of a clock pulse
Registers in the interface share a common
clock with CPU registers
Asynchronous Data Transfer
Internal timing in each unit (CPU and Interface)
is independent
Each unit uses its own private clock for internal
registers

## Slide 8: I/O Organization
Strobe : Control signal to indicate the time at which data is being transmitted
  Source-initiated strobe
  Destination-initiated strobe

## Slide 9: I/O Organization
Handshake: Agreement between two units
  Source-initiated

## Slide 10: I/O Organization
Destination initiated handshake

## Slide 11: I/O Organization
Asynchronous Data Transfer
Special bits are inserted at both ends of the character code
Each character consists of three parts :
start bit : always “0”, indicate the beginning of a character
character bits : data
stop bit : always “1”

## Slide 12: I/O Organization
Asynchronous transmission rules
  (1) When a character is not being sent, the line is kept in the 1-state
  (2) The initiation is detected from the start bit, which is always “0”
  (3) The character always follow the start bit
  (4) A stop bit is detected when the line returns to the 1-state for at least one bit time
  UART (Universal Asynchronous Receiver): 8250

## Slide 13: I/O Organization
Modes of Transfer
Data transfer to and from peripherals
1) Programmed I/O
2) Interrupt-initiated I/O
3) Direct Memory Access (DMA)
4) I/O Processor (IOP)

## Slide 14: I/O Organization
Example of Programmed I/O
Click to add text

## Slide 15: I/O Organization
Interrupt-initiated I/O
1) Non-vectored : fixed branch address
2) Vectored : interrupt source supplies the branch address
Priority Interrupt
Identify the source of the interrupts from simultaneous several sources
Determine which one is to be serviced first from simultaneous multiple requests

## Slide 16: I/O Organization
Software Polling
Identify the highest-priority source by software means
Polls the interrupt sources in sequence
The highest-priority source is tested first

## Slide 17: I/O Organization
Hardware priority interrupt
Daisy-Chaining, parallel priority
  Daisy -chaining

## Slide 18: I/O Organization
One step of DC
(1) No interrupt request
(2) Invalid : interrupt request, but no ack (3) No interrupt request: Pass to other device
(4) Interrupt request

## Slide 19: I/O Organization
Parallel Priority
Priority Encoder
Parallel Priority :
  Interrupt Enable F/F (IEN): set or cleared by program
  Interrupt Status F/F (IST): set or cleared by output

## Slide 20: I/O Organization
Interrupt Cycle
At the end of each instruction cycle, CPU
checks IEN and IST
if both IEN and IST equal to “1”
CPU goes to an Interrupt Cycle
  Sequence of microoperation during Interrupt cycle

## Slide 21: I/O Organization
Direct Memory Access (DMA)
DMA controller takes over the buses to manage the transfer directly between the I/O device and memory
Transfer Modes
  Burst transfer : Block
  Cycle stealing transfer : Word

## Slide 22: I/O Organization
DMA Controller (Intel 8237 DMAC) Initialization Process
1) Set Address register: memory address for read/write
2) Set Word count register: the number of words to transfer
3) Set transfer mode :
  read/write,
  burst/cycle stealing,
  I/O to I/O,
  I/O to Memory,
  Memory to Memory
  Memory search
  I/O search
4) DMA transfer start : next section
5) EOT (End of Transfer): Interrupt

## Slide 23: I/O Organization

## Slide 24: I/O Organization
DMA Transfer (I/O to Memory)
1) I/O Device sends a DMA request
2) DMAC activates the BR line
3) CPU responds with BG line
4) DMAC sends a DMA acknowledge to the I/O device
5) I/O device puts a word in data bus (memory write)
6) DMAC write a data to the address specified by AR
7) Decrement Word count register
8) Word count register = 0 (EOT interrupt)
9) Word count register ≠ 0 (DMAC checks the DMA request from I/O device)

## Slide 25: I/O Organization

## Slide 26: I/O Organization
Input-Output Processor (IOP)
Communicate directly with all I/O devices
Fetch and execute its own instruction
  IOP instructions are designed for I/O transfer
  DMAC must be set up entirely by the CPU
Designed to handle the details of I/O processing

## Slide 27: I/O Organization
Intel 8089 IOP